## Slide 1: IP Resource Certification
_________________________________________________
Andy Davidson adavidson@he.net
Hurricane Electric / LONAP / IXLeeds TREX Workshop 2011
16th September, Tampere, Finland

## Slide 2: Resource Certification
Overview
Certifying my resources with the RIPE NCC
Verifying other’s resources on my equipment

## Slide 3: We <3 routing, but we suck at it.
Accidental, huge customer impact
  YouTube, Pakistan Telecom
  AS7007
  Unfiltered customers getting IP transit
Deliberate, criminal activity?
  Defcon/Pilosov – stealing traffic
  Originating darknets for spam (blacklisting)
  L-Root clones, discovered with ICANN renumbered
Notes: AS7007 – black hole caused when MAI Network Services (7007) leaked deaggregated /24s of the whole internet, back to the internet. BGP->RIP->BGP. http://www.merit.edu/mail.archives/nanog/1997-04/msg00444.html

## Slide 4: Certificates x509v3 and ROAs
Who owns?
Which Resource?
When?
According to?

## Slide 5: ROA
Route Origin Authorisation
Not a certificate, a signed object.
Prefix holder’s explicit permission that a given prefix can be originated by a given ASN.
This gives me data to do Origin validation with.
SuperISP CA
___________________
10.0.0.0/8
AS65500
SuperISP EE
___________________
10.0.0.0/8
AS65500
ROA
___________________
10.0.0.0/8-16
AS65500

## Slide 6: 3 Step Process
SuperISP CA
___________________
10.0.0.0/8
AS65500
SuperISP EE
___________________
10.0.0.0/8
AS65500
ROA
___________________
10.0.0.0/8-16
AS65500
Build a CA
Sign an EE
Publish a ROA

## Slide 7
LIR PORTAL
Click on ‘Certification’
Your user needs Certification privs.

## Slide 8
Clicking through to build your CA also creates certificates for your aggregate resources.

## Slide 9
Drag and Drop your resources into the ROA Builder…

## Slide 13: How can I verify others’ ROA?
Router
ROA Cache
Publishing CA
Publishing CA
Publishing CA
Publishing CA
Routing Table
POLICY

## Slide 14
VALID
Matching ROA and AS Number
INVALID
Matching ROA found but AS number did not match!
NOT FOUND
No ROA
I can write policies on my router
which cause different behaviours
depending on the response from
my RPKI cache….

## Slide 15: Example Router Configuration
router bgp 10
bgp log-neighbor-changes
bgp rpki cache 192.168.10.10 port-number 32000 refresh-time 5
network 192.168.10.0
neighbor 192.168.0.2 remote-as 20
neighbor 192.168.0.2 soft-reconfiguration inbound
neighbor 192.168.0.6 remote-as 66
neighbor 192.168.0.6 soft-reconfiguration inbound
neighbor 192.168.0.6 route-map PERMIT-INVALID in
route-map PERMIT-INVALID permit 10
match rpki-invalid
set local-preference 50
Make a valid alternative prefix become best-path.

## Slide 16: Better Example with route-policy in XR
route-policy validity-0
if origin-validation-state is valid then
set local-preference 100
else set local-preference 50
endif
end-policy
route-policy validity-2
if origin-validation-state is valid then
set metric 100
elseif origin-validate-state is not-found
set metric 50
else set metric 25
endif
end-policy

## Slide 17: One day safe?
route-map validity-0
match rpki-invalid
drop
route-map validity-1
match rpki-not-found
set localpref 1
Maybe I want an certified peer pfx to score lower than a valid route from transit..
See ya, sucker!!!!

## Slide 18: Only import signed objects
route-map validity-0
match rpki-valid
set localpref 110
route-map validity-1
drop

## Slide 19: Open Source ROA Processor
Router
ROA Cache
Publishing CA
Publishing CA
Publishing CA
Publishing CA
Routing Table
POLICY
https://subvert-rpki.hactrn.net/
http://www.rpki.net/

## Slide 20: Not a magic bullet
Path Validation missing
  Still vulnerable to MITM attacks.
Early code from vendors
  Lots of testing work to do!
Address Policy, Trust relationships
  RPKI – is it an “off” switch for networks?
Huge and paranoid organisations will want to run their own CAs, not the RIR one.

## Slide 21
Questions ?
Feedback ?
Abuse ?