## Slide 1: IETF81 Secure IDR Rollup – TREX Workshop 2011
David Freedman, Claranet

## Slide 2: Introduction to Secure IDR (SIDR)
You are in a darkened room at the IETF.
You are surrounded by vendors.
A lone operator stands quietly in the corner…..

## Slide 3: A reminder of concepts.. RPKI
IANA are the numbering authority,
coordinating allocation of numbering
resources to Regional Internet Registries
The current situation
RIPE NCC are the Regional Internet Registry, providing numbering allocations and database services to Local Internet Registries.
Local Internet Registries are usually network operators, they consume allocated resources and use the database to build customer (and sometimes peer) filters.

## Slide 4: Simple filtering from the database
Q. Which routes should I accept from my customer AS8272?
A. Only 193.221.118.0/24
$ whois -r -Troute -i origin AS8272
% This is the RIPE Database query service.
% The objects are in RPSL format.
%
% The RIPE Database is subject to Terms and Conditions.
% See http://www.ripe.net/db/support/db-terms-conditions.pdf
% Note: this output has been filtered.
% To receive output for a database update, use the "-B" flag.
% Information related to '193.221.118.0/24AS8272'
route: 193.221.118.0/24
descr: CONVERGENCE
origin: AS8272
mnt-by: CONVERGENCE-MNT
org: ORG-CNV1-RIPE
source: RIPE # Filtered

## Slide 5: I have it too easy….
My customer has no downstreams
  This means no macro evaluation
I’m only filtering my customer
  Somebody I’m able to (somewhat) control the quality of the data held in the database before I build my filters (try doing this to peers, not much fun).
I’m an LIR of the RIPE NCC
  I actually have a great database from which to build such filters, other service regions are not as stringent with regards to this and as such, independent databases (such as Merit’s RADB and ALTDB) exist to bridge this gap (but being decoupled from the RIR, they can suffer from authority problems) – Nobody else has this great IP<->ASN binding.

## Slide 6: Why filter anyway?
Route Hijacking, two modern examples cited:
  Pakistan Telecom v Youtube [2008]
    Lack of filters by Upstreams (PCCW) allowed a leaked /24 for YouTube from Pakistan Telecom to propagate for over two hours, leading to a battle of Longest Prefix Match until the rogue announcement could be pulled.
  Kapela / Pilosov attack [2008]
    Hijack a route and use a crafted AS_PATH to blind selective transit networks on the return to the hijacked path (creating a MITM vector).
Need to verify the peer against the route and the AS_PATH somehow.
  This means having good, authoritative data.
  The system has to be easy to use and widely adopted
  The system has to scale.
We should just trust each other, right?

## Slide 7: Extended X.509 Certification Hierarchy
RFC3779 extensions in Cert carry IP/ASN information.
RFC5280 “Subject Information Access” extension defines publishing URI.
CA certificates issued downstream from the IANA through RIR and LIR participants.
Last CA in the chain issues an EE Certificate.
EE Certificate used to produce a RoA (just a signed blob).
draft-ietf-sidr-arch-13

## Slide 8: And we validate this how?
draft-ietf-sidr-rpki-rtr-16 explains:
  Periodically download entire copy of the RPKI with rsync (RFC5781)
  Offline validation into a trusted cache
  Router peers with cache using rpki-rtr protocol and receives trusted origin data.
Sounds futuristic?
  Cisco IOS and IOS-XR have PoC code running now
  Compute load demonstrated to be ~10µsec per update*
How much of this do I have to run myself?
  Options for RIR Hosted CA, RoA generator and publisher
  Perhaps your upstream can provide a cache if you are small?
* Source: http://ripe60.ripe.net/presentations/Bush-The_RPKI_Origin_Validation.pdf

## Slide 9: What do we do with this?
Local operator decision
  Prefer valid over unvalidated over invalid for instance*
RP/0/1/CPU0:r0.dfw#show bgp 192.158.248.0/24
BGP routing table entry for 192.158.248.0/24
Versions:
Process bRIB/RIB SendTblVer
Speaker 132327 132327
Last Modified: Oct 2 01:06:47.630 for 13:33:12
Paths: (6 available, best #3)
Advertised to peers (in unique update groups):
204.69.200.26
Path #1: Received by speaker 0
2914 1299 6939 6939 27318
157.238.224.149 from 157.238.224.149 (129.250.0.85)
Origin IGP, metric 0, localpref 100, valid, external, \
origin validity state: valid
Community: 2914:420 2914:2000 2914:3000 4128:380
Path #2: Received by speaker 0
...
* Example courtesy of : http://ripe60.ripe.net/presentations/Bush-The_RPKI_Origin_Validation.pdf
draft-ietf-sidr-origin-ops-10

## Slide 10: BGPSec
Without AS_PATH filtering everywhere, prefixes and their origin ASNs can be hijacked.
  RoA still valid as Origin ASN hasn’t changed.
Need path validation in the BGP as well
  BGPSec being developed by SIDR, draft-ietf-sidr-bgpsec-overview-00
BGPSec introduces new type of certificate
  New “Router” certificate, public key published for an AS, private key held by routers within the AS, draft-ietf-sidr-bgpsec-overview-00.
Routers use private keys to sign AS_PATH elements
  New attribute BGPSEC_Path_Signatures*
^A0.RtrCert
Sig0
Exp Time
Algo ID
^A1.RtrCert
Sig1
ASN 0
ASN 1
AS_Seq
* Example courtesy of : http://tools.ietf.org/agenda/81/slides/sidr-10.pdf

## Slide 11: But what about?
AS_PATH prepending?
  Suggested to add pCNT counter of prepends, decouple policy from path*
Transparent Route Servers (i.e MLP)?
  This makes people uneasy as it proposes a bypass mechanism
  Current thinking to use pCNT=0 as “Special Case” for xref with AS_PATH, meaning “ignore this AS in AS_PATH when bestpathing” , non-BGPSec speakers simply strip the pCNT=0 AS from the AS_PATH completely.
AS1 Path Signature
Hash(…) Signed by Router
Key AS1.rtr-yy  Sig1
AS0 (origin) Path Signature
Hash(…) Signed by
Router Key AS0.rtr-xx  Sig0
AS1
AS2
Algo ID
Algo ID
NLRI
AS0
AS1
Sig0
Sig1
Exp Time
pCNT
pCNT
* Example courtesy of : http://tools.ietf.org/agenda/81/slides/sidr-10.pdf
Some as-yet undrafted ideas

## Slide 12: And what about replay attacks?
Replay attacks are of concern
  Provider annoyed at customer who switches
  Prefix “Stuck in Router” being replayed over and over again.
  All at Human timescales.
Freshness is critical
  We could do smaller signing lifetimes
  Origin could re-announce before this expires (i.e Beaconing)
  Suggested to be days, but can be hours for critical infrastructure)
  Timing is of course jittered.
Beaconing is required to prevent replay attacks
  But only origin beaconing is tolerable to internet infrastructure
  Multi-Beaconing neither useful, nor affordable.
draft-ietf-sidr-bgpsec-ops-00

## Slide 13: More SIDR discussed topics
draft-ietf-sidr-algorithm-agility-03
  How we transition to newer and more secure algorithms without disruption.
  We already have normal Key Rollovers (i.e old key expires or needs to be revoked)
  This draft specifies a rollover for reason of a new algorithm.
  Five Phases (0-4) with six steps:
    Phase 0: Old algorithm only used.
    Phase 1: Parent CAs can issue using new algorithm.
    Phase 2: RPs MAY be able to validate new algorithm.
    Phase 3: RPs MUST be able to validate new and old algorithms.
    Phase 4: RPs MAY be able to validate using old algorithm.
    Phase 0: Return to Phase 0, only now old algorithm is invalid.

## Slide 14: More SIDR discussed topics
draft-ietf-sidr-publication-01
  An XMLoHTTP based publication protocol, designed for children publishing back to parents (think outsourced SIA model).
draft-ietf-sidr-usecases-02
  A brilliant reference document showing various RPKI use cases and their outcomes. I would recommend a read of this, here is an except of the index:
3. Origination Use Cases . . . . . . . . . . . . . . . . . . . . 6
3.1. Single Announcement . . . . . . . . . . . . . . . . . . . 6
3.2. Aggregate with a More Specific . . . . . . . . . . . . . . 7
3.3. Aggregate with a More Specific from a Different ASN . . . 7
3.4. Sub-allocation to a Multi-homed Customer . . . . . . . . . 8
3.5. Restriction of a New Allocation . . . . . . . . . . . . . 9
3.6. Restriction of New ASN . . . . . . . . . . . . . . . . . . 10
3.7. Restriction of a Part of an Allocation . . . . . . . . . . 10
3.8. Restriction of Prefix Length . . . . . . . . . . . . . . . 11
3.9. Restriction of Sub-allocation Prefix Length . . . . . . . 12
3.10. Aggregation and Origination by an Upstream . . . . . . . . 13

## Slide 15: And finally some fun
draft-ietf-sidr-ghostbusters-09
  With all these certificates floating around, when there’s a problem, who you gonna call?
  This stuff may not be engineered by neteng/netops folk, perhaps systems/security people, not traditionally ops contacts from external networks!
  We sign RoAs with our EE certificates, why limit this to just routing data?
  Use the EE to sign a vCard, for somebody to contact regarding a RoA or certification chain.
  Not meant to replace WHOIS
BEGIN:vCard
VERSION:4.0
FN:Human's Name
N:Name;Human's;Ms.;Dr.;OCD;ADD
ORG:Organizational Entity
ADR;TYPE=WORK:;;42 Twisty Passage;Deep Cavern; WA; 98666;U.S.A.
TEL;TYPE=VOICE,MSG,WORK:+1-666-555-1212
TEL;TYPE=FAX,WORK:+1-666-555-1213
EMAIL;TYPE=INTERNET:human@example.com
END:vCard

## Slide 16
Any questions?
Notes: 16